## Slide 1: ANTENNA THEORY AND SIMULATION (YAGI)
SSP MINI PROJECT
BY-VINEET GALA
(COMM SUBSYSTEM)

## Slide 2: Aim Of The Project
To simulate the Yagi antenna (ground station) for 145 Hz frequency and analyze results.
Study factors which antenna parameters depend on.

## Slide 3: Approach
Read about antenna parameters and theory associated.
Referred a couple of tutorials on HFSS.
Got used to HFSS by making simple antenna models and proceed step by step.
Structured and planned simulations for different configurations of antenna.

## Slide 4: About Antennas
How antennas work?
Antenna parameters-
Gain
Radiation Pattern
Directivity
S11

## Slide 5: More About Antennas
Dipole antenna
Yagi antenna
Why use a Yagi antenna?

## Slide 6: Achieving The First Milestone
By the end of week 1, I made a simple dipole antenna powered by source via a coaxial cable.
I learnt how to simulate and how to view and analyse results of the simulation such as S11 for different antenna lengths (optimetrics), gain etc.

## Slide 7: Achieving The Second Milestone
By the end of second week, I made a simple Yagi antenna model and started simulations
What difference does a reflector and 1, 2, 3 directors make?
Antenna | Maximum Gain (dB)
Dipole | 2.3805
Yagi (1 reflector, 1 director) | 7.1425
Yagi (1 reflector, 2 directors) | 7.6902
Yagi (1 reflector, 3 directors) | 8.0146

## Slide 8
Dipole
Yagi – 1 ref, 1 dir
Yagi – 1 ref, 2 dir
Yagi – 1 ref, 3 dir
Radiation
Patterns

## Slide 9: Achieving The Final Milestone
Added the boom to the setup but faced problems (for later).
Simulated the antenna for different distances of reflector, directors from feed pole.

## Slide 10: Analysis
Reflector Distance (mm) | Maximum Gain (dB)
735 | 7.6799
740 | 7.6902
745 | 7.6485
750 | 7.6324
Dir 1 Distance (mm) | Dir 2 Distance (mm) | Maximum Gain (dB)
270 | 680 | 7.6687
250 | 680 | 7.6794
270 | 660 | 7.5824
250 | 660 | 7.5997
258.75 | 672.75 | 7.6120

## Slide 11: Problems
Unavailability of HFSS license initially.
Unable to simulate the Aluminium Boom.
Long time taken for simulating models with optimetrics – which failed because I could not see the results for the concerned variable.
Garbage reports popping up due to some small mistakes.

## Slide 12: Takeaway Lessons
Most of what I know about wireless communication.
Tracked satellites and received information.
Other subsystems’ work.
Managing time, sleep and academics.
Working in a team and being answerable for my work – being consistent.

## Slide 13: Feedback
The Mini Project and Recruitment Process:
  Busiest and most productive 3 weeks so far.
  A very good idea to introduce a newcomer to the ways of the team.
Mentor: Atharv Savarkar
  Go-to Person for any problems related to my Mini Project at anytime.
  Understanding and helpful.

## Slide 14: THANK YOU!

## Slide 15: APPENDIX

## Slide 18
https://github.com/vineetgala/SSP_Mini_Project